## Slide 1: Fine-Grained, Multi-Domain Network Resource Abstraction as a Fundamental Primitive to Enable High-Performance, Collaborative Data Sciences
Qiao Xiang12, J. Jensen Zhang12, X. Tony Wang1, Y. Jace Liu1,
Chin Guok3, Franck Le4, John MacAuley3, Harvey Newman5, Y. Richard Yang12
1Tongji University, 2Yale University, 3 Lawrence Berkeley National Laboratory,
4IBM T.J. Watson Research Center, 5California Institute of Technology,
11/13/2018, Dallas, ACM/IEEE SuperComputing'18

## Slide 2: Background
Today's premier science experiments rely on finely-tuned workflows that coordinate geographically distributed resources.
Large Hadron Collider
Square Kilometre Array
Linac Coherent Light Source
Figure sources: phys.org, extremetech.com

## Slide 3: Example: Compact Muon Solenoid (CMS) Experiment in Large Hadron Collider (LHC)
Large raw datasets from LHC at the Tier-0 site
RECO and AOD datasets are distributed to Tier-1 sites
RECO, AOD and simulation datasets are transferred among Tier-1~3 sites for analysis.
RAW Data: tens of PB per year
RECO and AOD: multiple times of RAW data depending on analysis requirements
The key to supporting these distributed resource workflows is the ability to reserve and guarantee bandwidth across multiple network domains to facilitate predictable end-to-end network connectivity.

## Slide 4: Multi-domain Circuit Reservation Systems
Several multi-domain network resource reservation systems are being deployed, driven by the demand and substantial benefits of providing predictable network resources.
  Example: OSCARS [1]
A network interface is provided for users to submit requests for reserving a specific amount of bandwidth, and return either success or failure.
[1] On-Demand Secure Circuits and Advance Reservation System: http://es.net/engineering-services/oscars/
Reservation System
Circuit set,
Bandwidth Values
User
Success / Failure
Network

## Slide 5: Inefficiency of Reservation Systems: Example
For a set of circuits (S, D1), (S, D2) and (S, D3), how much bandwidth can the user reserve?
D2
D3
D1
S
40Gbps
40Gbps
10Gbps
10Gbps
Member Network 1
Member Network 2
Member Network 3
100Gbps
10Gbps
100Gbps
10Gbps
10Gbps
100Gbps
How about now?
Sequential, cut-by-half-until-reserved:
12 reserve attempts to reach
(S, D1): 8.33 Gbps;
(S, D2): 8.33 Gbps;
(S, D3): 1.04 Gbps
A fair optimal solution
(S, D1): 10 Gbps
(S, D2): 5 Gbps
(S, D3): 5 Gbps
The lack of visibility of network state (topology, policy and etc.) leads to substantial inefficiency of network resource reservation systems.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 6: Mercator: A Multi-Domain Network Resource Discovery System
Goal: Provide fine-grained, global network resource information, to optimize large-scale, multi-domain data transfers.
User submits a resource discovery request of a set of circuits to a logically centralized aggregator;
Aggregator decomposes the request and forwards it to Mercator domain servers at networks;
Mercator servers compute, obfuscate and return resource abstraction to aggregator
Aggregator composites the information and returns to user;
User computes and sends reservation requests to reservation systems at networks.
Step 5
Notes: Our idea: on-demand, partianl-instantiation

## Slide 7: Mercator: Key Components
Resource abstraction: Use linear inequalities to provide a compact representation of multi-domain network available bandwidth.
Resource abstraction obfuscating: Merge the resource abstraction of multiple domains without revealing the abstraction of individual domain.
Super-set projection: Improve the system scalability via pre-computation and projection.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 8: Resource Abstraction
Basic idea: Use linear inequalities to provide a compact representation of multi-domain network available bandwidth.
100
100
Geometrically, resource abstraction represents the bandwidth feasible region of network for providing bandwidths to this set of circuits.
Redundant inequalities are removed via a polynomial-time, optimal algorithm.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 9: Can Resource Abstraction Handle Non-Unicast Circuits?
Basic idea: introduce auxiliary variables and additional equations.
Multicast circuit

## Slide 10: Resource Abstraction: Multi-Path Circuit

## Slide 11: Resource Abstraction: Weight-Cost Multi-Path Circuit
Network M1: Split the traffic of (S1, e1), (S1, e2) in a ratio of 1:2

## Slide 12: Resource Abstraction: Accuracy
Resource abstraction provides a compact, accurate representation of multi-domain network available bandwidth.
Step 5
A fair optimal solution:
Notes: Our idea: on-demand, partianl-instantiation

## Slide 13: Resource Abstraction: Privacy Concern
Resource abstraction represents the bandwidth feasible region of network for providing bandwidths to this set of circuits.
  Such regions are also private information.
  Aggregator becomes single point of failure.
Step 5
Notes: Our idea: on-demand, partianl-instantiation

## Slide 14: Mercator: Key Components
Resource abstraction: Use linear inequalities to provide a compact representation of multi-domain network available bandwidth.
Resource abstraction obfuscating: Merge the resource abstraction of multiple domains without revealing the abstraction of individual domain.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 15: Resource Abstraction Obfuscating Protocol
Goal: Merge the resource abstraction of networks without revealing the bandwidth feasible region of any individual domain.
Security model: Semi-honest (honest but curious).
Basic idea: Each domain obfuscates its own state with a private random matrix and a couple of shared random matrices.
AS2

## Slide 16: Resource Abstraction Obfuscating Protocol: Specification
  Initialization: All networks agree on . Each network generates:
    : a -by- random matrix private to network ;
    , : two -by- random matrices shared with network .
  Augmentation: Each network transforms into augment form ;
  Obfuscation: Each network sends the obfuscated resource abstraction to the aggregator:
  Collection: Aggregator sums up all received resource abstraction:
Theorem: Given , the obfuscating protocol yields equivalent to , but ensures no network/user can associate any inequality in to any specific domain.

## Slide 17: Resource Abstraction Obfuscating Protocol: Example
Mercator Server 1
Mercator Server 2
Mercator Server 3
Aggregator
Maximizing subject to either feasible region would get the optimal solution .

## Slide 18: Resource Abstraction: Scalability Concern
Issue: Computing and collecting resource abstraction for each request from scratch is expensive, and therefore may not be scalable.
  Bottleneck: communication between Mercator domain servers and aggregator
Step 5

## Slide 19: Mercator: Key Components
Resource abstraction: Use linear inequalities to provide a compact representation of multi-domain network available bandwidth.
Resource abstraction obfuscating: Merge the resource abstraction of multiple domains without revealing the abstraction of individual domain.
Super-set projection: Improve the system scalability via pre-computation and projection.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 20: Resource Abstraction Super-Set Projection
Basic idea: Proactively discover the resource information for a set of circuits between every pair of source and destination networks, and project the collected information to derive the responses to user’s requests.
Example: Aggregator proactively discovers the resource abstraction for circuits between 3 member networks.
What is the resource information of two circuits: one from M1 to M2, and one from M2 to M3.
Aggregator

## Slide 21: Performance Evaluation
Topology: LHCONE: a science federation network of 62 member networks
  Intradomian topology: randomly chosen from Topology Zoo
Traffic: 48-hour CMS trace data
Metrics: throughput, fairness, latency, scalability, …

## Slide 22: Benefits of Mercator
Objective: max-min fairness
Objective: total throughput
An average of 2x improvement of fairness
An average of 15% improvement of throughput

## Slide 23: Benefits of Mercator
An average of 100x improvement of resource discovery latency
Probe-requests-based systems have an average of 73% request failure ratio.
Resource discovery latency
Request failure ratio of probe-requests-based systems

## Slide 24: Efficiency of Resource Abstraction Obfuscating
Obfuscating latency
Obfuscated data transmission
The resource abstraction obfuscating protocol scales to up to 200 member network.

## Slide 25: Efficiency of Super-Set Projection
Scalability via super-set projection
Update latency
Super-set projection decreases the average resource discovery latency by around 2 times, and scales to up to 200 member network.

## Slide 26: Summary
The lack of visibility of network state (topology, policy and etc.) leads to substantial inefficiency of network resource reservation systems.
We design Mercator, a multi-domain network resource discovery System, to provide fine-grained, global network resource information, to optimize large-scale, multi-domain data transfers.
Key components:
  Resource abstraction: Use linear inequalities to provide a compact representation of multi-domain network available bandwidth domains.
  Resource abstraction obfuscating: Merge the resource abstraction of multiple domains without revealing the abstraction of individual domain.
  Super-set projection: Improve the system scalability via pre-computation and projection
Demonstration at SC'18
  When: Tuesday – Thursday during SC'18 week
  Where: Booth 1413 (Caltech Booth)
  What: Multi-domain routing discovery and resource orchestration
  Contact: Qiao Xiang (qiao.xiang@cs.yale.edu)